## Slide 1: Project 3(CS472 A1 Computer Architecture)
Pipelined Datapath– Project 3 Review Session
04/04/2024
Yeryoung Kim

## Slide 2: Contents
  1. Simulation Framework
  - Main memory & Simulated Registers
  - Read & Write Registers
  - Create big loop based on Clock cycle.
  - Five stages Methods
  2. Output examples of Pipelined Datapath simulation
  3. Q&A

## Slide 3: Pipelined Datapath
Notes: IF stage()
- Instruction Fetch from the Instruction Cach
(input array for your code)
- Write the Fetched instruction to IF/ID Write register.

## Slide 4: Main Memory and simulated Registers
Initialization on Main_Mem and simulated Register
Main_Mem[0]=0,Main_Men[1]=1,… Main_Mem[0XFF]=FF
Example of C++: int Regs[32]
Initial value = 0x100 +Register number
$0 = 0,$1=0x101 ,$2=0x102,…$31 =0x11f.

## Slide 5: Five stages sequence Methods
IF_stage() : Instruction fetch
ID_stage(): Instuction decode/ register file read
EX_stage(): Execute/ address calculation
MEM_stage(): Memory access
WB_stage(): Write back to Register file
Print_out_everything(): Print the Regs[32] values and both the Read and Write version of all four pipeline registers
Copy_write_to_read(): Copy all information from Write version of pipeline registers to Read version of pipeline registers.

## Slide 6: 1. Simulation Framework
<Pipeline Datapath>
Implant your `Disassembler` program from Project 1
32-bit instruction and extract the opcode, two source reg #s,
two possible write reg #s, the function code, and the offset.
‘InstructionsCache Array’ to put all 12 instructions
Read and Write versions of 4 pipelined Registers
<Your choice of Big loop>
(1 loop =1 clock cycle)
IF_stage();
ID_stage();
EX_stage();
MEM_stage();
WB_stage();
Print_out_everything();
Copy_write_to_read();

## Slide 7
Write
IF/ID Register
Readx
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
IF stage()
ID stage()
EX stage()
MEM stage()
WB stage()
Registers
Four pipeline Registers
Method
- Fetched 0x00a63820 [add, $7, $5, $6]
-NOPs
-NOPs
-NOPs
-NOPs
Clock Cycle 1
<InstructionsCache Array>
0x00a63820 [add, $7, $5, $6]
0x8d0f0004[lw,$15,4,($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022[sub,$10,$3,$2]
0x10c8fffb [beq,$6,$8,label]
Main Memory(Data Cache)

## Slide 8: Print out everything()
+ Reg[32] values

## Slide 9
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
Four pipeline Registers
Method
Clock Cycle 1
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
Copy write to read()
- Copy information from the write pipeline registers
to the read pipeline registers

## Slide 10
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
IF stage()
ID stage()
EX stage()
MEM stage()
WB stage()
Four pipeline Registers
Method
Clock Cycle 2
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
- Fetched 0x8d0f0004 [lw, $15, 4, ($8)]
- Access IF/ID Read pipeline register
- Decode Fetched instruction
- Read the register files
- Generate the control bits
Registers
-NOPs
-NOPs
-NOPs
Main Memory(Data Cache)
(Instruction: 0x00a63820)

## Slide 11: Reference Materials for the control signal

## Slide 12: Reference Materials for the control signal
Notes: You are using ALU action column.

## Slide 13
+ Reg[32] values

## Slide 14
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
Four pipeline Registers
Method
Clock Cycle 2
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
Copy write to read()
- Copy information from the write pipeline registers
to the read registers

## Slide 15
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
IF stage()
ID stage()
EX stage()
MEM stage()
WB stage()
Four pipeline Registers
Method
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
- Fetched 0xad09fffc [sw, $9,-4,($8)]
- Access IF/ID Read pipeline register
- Decode Fetched instruction
- Read the register files
- Generate the control bits
- Access ID/EX Read Register
- Calculate the address with requested operation
- Write the appropriate value on Write pipeline register
(Instruction: 0x8d0f0004)
(Instruction: 0x00a63820)
Registers
-NOPs
-NOPs
Main Memory(Data Cache)
Clock Cycle 3

## Slide 16
+ Reg[32] values

## Slide 17
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
Four pipeline Registers
Method
Clock Cycle 3
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
Copy write to read()
- Copy information from the write pipeline registers
to the read pipeline registers

## Slide 18
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
IF stage()
ID stage()
EX stage()
MEM stage()
WB stage()
Four pipeline Registers
Method
Clock Cycle 4
- Fetched 0x00625022 [sub, $10, $3 ,$2]
- Access IF/ID Read pipeline register
- Decode Fetched instruction
- Read the register files
- Generate the control bits
- Access ID/EX Read pipeline Register
- Calculate the address with requested operation
- Write the appropriate value on Write pipeline register
(Instruction: 0xad09fffc)
(Instruction: 0x8d0f0004)
(Instruction: 0x00a63820)
- In case of `lb` Instruction ,use ALU result as
an index of Main memory and take the value
from the Main memory
- Otherwise, pass information to MEM_WB Write pipeline register.
-NOPs
Registers
Main Memory(Data Cache)
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]

## Slide 19
+ Reg[32] values

## Slide 20
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
Four pipeline Registers
Method
Clock Cycle 4
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
Copy write to read()
- Copy information from the write pipeline registers
to the read pipeline registers

## Slide 21
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
IF stage()
ID stage()
EX stage()
MEM stage()
WB stage()
Registers
Main Memory(Data Cache)
Four pipeline Registers
Method
Clock Cycle 5
- Fetched 0x10c8fffb
- Access IF/ID Read pipeline register
- Decode Fetched instruction
- Read the register files
- Generate the control bits
- Access ID/EX Read pipeline Register
- Calculate the address with requested operation
- Write the appropriate value on Write pipeline register
(Instruction: 0x00625022)
(Instruction: 0xad09fffc)
(Instruction: 0x8d0f0004)
- In case of `lb` Instruction ,use ALU result as
an index of Main memory and take the value
from the Main memory
- Otherwise, pass information to MEM_WB Write pipeline register.
(Instruction: 0x00a63820)
- Write information based on MEM/WB pipeline Register to register files
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]

## Slide 22
+ Reg[32] values

## Slide 23
Write
IF/ID Register
Read
Write
ID/EX Register
Read
Write
EX/MEM Register
Read
Write
MEM/WB Register
Read
Four pipeline Registers
Method
Clock Cycle 5
< InstructionsCache Array >
0x00a63820 [add, $7, $5, $6]
0x8d0f0004 [lw, $15, 4, ($8)]
0xad09fffc [sw, $9,-4,($8)]
0x00625022 [sub, $10, $3 ,$2]
0x10c8fffb [beq, $6, $8 ,label]
Copy write to read()
- Copy information from the write pipeline registers
to the read pipeline registers

## Slide 24: Reference Materials

## Slide 25
Q&A